Lab 3
Seven segment display
Manupriya Gupta 2018CS10355
Muskan Himmatsinghka 2018CS10359
This design of seven segment display enables us to display a particular decimal digit on the digital seven segment display on Basys3 board.
We made logic circuits for each component of the digital display as to when they should light up for displaying a particular number. This logic we arrived at using K map technique.
Only one anode was made active and the cathode bit value based on the schematic diagram.
The following were the test cases :
0000 0
0000 1
0010 2
0011 3
0100 4
0110 6
0111 7
1000 8
1001 9
0101 5
LHS if the table contains input in order of b0,b1,b2,b3 and RHS contains what is displayed on the digital display.